德国KSL试验粉尘系列介绍：

1/ Arizona dust SAE J726 fine  Arizona-Staub SAE J726 fein试验粉尘

2/ Arizona dust SAE J726 coarse  Arizona-Staub SAE J726 grob试验粉尘

3/ Talkumstaub gemäß DIN EN IEC 60529, VDE 0470 Talc dust according DIN EN IEC 60529, VDE 0470试验粉尘

4/ Prüfstaub gemäß DIN 40050试验粉尘

Teil 9 Pkt. 7.3.1. Test dust according to DIN 40050 Part 9 Point 7.3.1.

5/ Blowing Dust gemäß MIL-STD-810 Blowing Dust in accordance with MIL-STD-810试验粉尘

Test dust for testing according to MIL-STD-810G w/CHANGE 1

Method 510.6 Point 4.1.1.4 d. (2)

6/ Blowing Sand gemäß MIL-STD-810 Blowing Sand in accordance with MIL-STD-810试验粉尘

Test dust for testing according to MIL-STD-810G

Method 510.6 Point 4.2.1.3

7/ Prüfstaub DIN EN 60068-2-68 Test Dust DIN EN 60068-2-68试验粉尘

for tests in accordance to Point 6.1.4.1. Variant 3 Sand

for test method Lc1 material: Quartz SiO2

8/ Settling Dust gemäß MIL-STD-810 Settling Dust in accordance with MIL-STD-810试验粉尘

Test dust for testing according to MIL-STD 810F

Method 510.4 Point 2.3.2.5. c

9/ Prüfstaub gemäß ECE R 45 Regelung Nr. 45, Revision 2试验粉尘

Anhang 4 Punkt 2.1.1  Anhang 4 Punkt 2.1.2

Test dust according ECE R 45

Regulation No. 45, Revision 2

Annex 4, Point 2.1.1

Annex 4, Point 2.1.2

10/ Prüfstaub DIN EN 60068-2-68 Test Dust DIN EN 60068-2-68试验粉尘

for tests in accordance to Point 6.1.4.1. Variant 2 Coarse Dust

for test method Lc1 material: Quartz SiO2

11/ Prüfstaub China fein, mittel, grob Test dust China fine, medium, coarse试验粉尘

12/ Portlandzement Portland cement试验粉尘

Cement for Building technology / structural engineering Is an inorganic finely ground, hydraulically acting binder for mortar and concrete, which is also used as a test dust.

Portland cement is, for example, listed in the Standard JIS Z8901 Class 6.

The Portland cement used by us complies with DIN EN 197-1 and the type of cement CEM II/A-LL (Portland limestone cement) The main component is Portland cement clinker 6-20 % by mass of limestone

13/ Flugasche Fly ash试验粉尘

Coal fly ash is used for example in cement as a mineral raw material and building material, in bound and unbound form.

The product has no hazardous properties and is also used as test dust. Fly ash is described for example in JIS Z8901 Class 5.

14/ Prüfstaub / Test dust KSL 14081试验粉尘

based on analyses for Chinese dust, synthetically produced, developed for Roof Systems

15/ Prüfstaub Brasil / Test Dust Brasil试验粉尘

Typ M1 Typ M2 Typ M3 Typ M6 Typ M7 Typ M9

16/ Arizona-Staub extra grob试验粉尘

17/ Arizona dust extra coarse试验粉尘

18/ Prüfstaub / Test dust KSL 12050试验粉尘

zur Simulation von hohem Verschleiß / for the simulation of high wear

19/ Prüfstaub / Test dust KSL 14083试验粉尘

Indien-Staub S-P007/3 (synthetisch hergestellt)

für Prüfungen im Automobilbereich

Indian dust S-P007/3 (synthetic Test dust) for tests in the automotive field

20/ Prüfstaub / Test dust KSL 14084试验粉尘

Brasilien-Staub S-P007/4 (synthetisch hergestellt)

für Prüfungen im Automobilbereich

Brasil dust S-P007/4 (synthetic Test dust) for tests in the automotive field

21/ Prüfstaub Brasil / Test Dust Brasil试验粉尘

Typ M4 Typ M5 Typ M8 Typ M10 / KSL 12050

22/ Prüfstaub KSL 11046 Test dust KSL 11046试验粉尘

23/ Prüfstaub KSL 11047 Test dust KSL 11047试验粉尘

24/ Prüfstaub KSL 11047-B Test dust KSL 11047-B试验粉尘

25/ Prüfstaub KSL 14017 Test dust KSL 14017试验粉尘

26/ Prüfstaub KSL 14019 Test dust KSL 14019试验粉尘

27/ Prüfstaub / Test dust KSL 14078试验粉尘

Prüfstaub / Test dust KSL 14079

Alternative zu Prüfstaub China fein! / Alternative to Test dust China fine!

28/ Prüfstaub KSL 14027 Test dust KSL 14027试验粉尘

Arizona-Staub SAE J726 fein   Arizona dust SAE J726 coarse  Arizona-Staub SAE J726 grob

Talkumstaub gemäß DIN EN IEC 60529, VDE 0470 Talc dust according DIN EN IEC 60529, VDE 0470  Prüfstaub gemäß DIN 40050 Teil 9 Pkt. 7.3.1. Test dust according to DIN 40050 Part 9 Point 7.3.1.  Blowing Dust gemäß MIL-STD-810 Blowing Dust in accordance with MIL-STD-810  Blowing Sand gemäß MIL-STD-810 Blowing Sand in accordance with MIL-STD-810 Test dust for testing according to MIL-STD-810G Prüfstaub DIN EN 60068-2-68 Test Dust DIN EN 60068-2-68  Settling Dust gemäß MIL-STD-810 Settling Dust in accordance with MIL-STD-810 Prüfstaub gemäß ECE R 45 Regelung Nr. 45, Revision 2 Prüfstaub DIN EN 60068-2-68 Test Dust DIN EN 60068-2-68

Prüfstaub China fein, mittel, grob Test dust China fine, medium, coarse Portlandzement Portland cement Flugasche Fly ash Prüfstaub / Test dust KSL 14081 Prüfstaub Brasil / Test Dust Brasil Typ M1 Typ M2 Typ M3 Typ M6 Typ M7 Typ M9 Arizona-Staub extra grob Arizona dust extra coarse

Prüfstaub / Test dust KSL 12050 Prüfstaub / Test dust KSL 14083 Indien-Staub S-P007/3 (synthetisch hergestellt) für Prüfungen im Automobilbereich Indian dust S-P007/3 (synthetic Test dust) for tests in the automotive field Prüfstaub / Test dust KSL 14084 Brasilien-Staub S-P007/4 (synthetisch hergestellt) für Prüfungen im Automobilbereich Brasil dust S-P007/4 (synthetic Test dust) for tests in the automotive field Prüfstaub Brasil / Test Dust Brasil Typ M4 Typ M5 Typ M8 Typ M10 / KSL 12050  Prüfstaub KSL 11046 Test dust KSL 11046 Prüfstaub KSL 11047 Test dust KSL 11047 Prüfstaub KSL 11047-B Test dust KSL 11047-B Prüfstaub KSL 14017 Test dust KSL 14017 Prüfstaub KSL 14019 Test dust KSL 14019 Prüfstaub / Test dust KSL 14078 Prüfstaub / Test dust KSL 14079 Alternative zu Prüfstaub China fein! / Alternative to Test dust China fine! Prüfstaub KSL 14027 Test dust KSL 14027

PTI粉尘灰灰尘ACFTD灰尘ISO 12103-1 A2 Fine Test Dust A2粉 ISO 12103-1 A4 Coarse Test Dust A4粉 ISO 12103-1 A3 Medium Test Dust A3粉MTD粉尘 Arizona Test Dust Fractions 亚利桑那试验粉尘MIL 810E4 Silica Sand & Dust Iron Oxide 波特兰水泥 Type I Glass Beads 玻璃珠 PV 树脂(喷融树脂) 汽车安全带测试粉尘ECE R16, Section 7.6.3.2 (GB 14166, Section 5.6.3.2液SoftC-2A Quartzose Mineral Dust DMT emission test dust (IEC 60312 5.1.2.5) Test Dust Type 8® DMT test dust type 8 (IEC 60312 5.1.2.3) Quartzose Mineral DMT carpet test dust (IEC 60312 5.1.2.2) DMT Dolomite Sand (IEC 60312 5.1.2.1)A2 ISO 细灰 A4粗灰 亚利桑那沙子亚利桑那试验粉尘 美国ISO MTD粉尘A2测试粉A3中级试验粉尘AC DUST A2 粉尘 ISO 试验粉尘 亚力桑那A2粉尘 美国PTI碳黑粉尘 ISO 12103-2 M2铝粉 A2 ISO 细灰 ISO 12103-2 M3铝粉 ISO 12103-2 M4铝粉ISO 12103-2 M5铝粉JIS CLASS 2级粉尘 PTI 粉尘Nominal 0-5 Arizona Test Dust PTI 粉尘Nominal 10-20 Arizona Test Dust PTI 粗粉 PTI 粉尘Nominal 20-40 Arizona Test Dust 试验用粉尘12103-1 A2类粗粉粗灰美国亚利桑那A1粉 FLY ASH 飞灰Portland Cement波特兰水泥美国亚利桑那M5粉APPIE JIS Z 8901 CLASS 1 试验粉尘APPIE JIS试验用粉体1 8种APPIE关东粉APPIE JIS test powders 1 class8 日本粉体工业技术协会APPIE APPIE JIS Z 8901 试验用粉体1，CLASS 8 APPIE JIS Z 8901 CLASS 15粉尘COTTON LINTERS 棉花纤维铁粉(赤)氧化铁 Carbon Black炭黑Ashrae test dust with carbon black 試験用粉体１の7種, 8種, 11種JIS粉尘是依据JIS(Japanese Industrial Standard，即日本工业标准)生产的试验粉尘，常被用于一些日系产品的检测。本公司可为广大国内用户提供日本进口的下述检测杂质，包括JIS Z 8901的试验粉尘和玻璃珠产品；请在与我们联系的时候描述清楚您需要的是下面哪种产品Quartz sand Talc Fly ash KANTO (Japanese) loam Carbon black Calcium- carbonate (heavy) Glass beads GBL type Glass beads GBM type White fused alumina JIS Z8901 1 种(硅砂) JIS Z8901 3 种(硅砂)JIS Z8901 4 种(滑石粉)JIS Z8901 7 种(关东粉)JIS Z8901 8 种(关东粉)铁粉0-5微米Fe3O4铁粉(赤)0-5微米Fe2O3 铁粉(赤)5-10微米Fe2O3 棉花纤维COTTON LINTERS

德国KSL Eskal 300, Eskal 500, Eskal 10, Eskal 15, Eskal 20, Eskal 30, Eskal 45, Eskal 60, Eskal 80, Eskal 150 fractions of natural calcium carbonate德国KSL Esstar 15, Esstar 20, Esstar 30, Esstar 45, Esstar 80 fractions of native starch德国KSL Eszet 15, Eszet 20, Eszet 30, Eszet 45, Eszet 80 fractions of sugar德国KSL Esqua fractions of quartz SiO2德国KSL Arizona staub fine/coarse synthetic,according SAE J 726B Rev,Jun.93 Table 4德国KSL Quarzstaub according ECE 6-16德国KSL Talkumstaub according IEC 529,EN 60529,DIN VDE 0470 Tell 1德国KSL Prufstaub nach DIN 40050喷灰装置 喷灰器 喷沙尘工具 喷试验粉尘装置 喷试验粉尘器 喷试验粉尘工具