公司地址：深圳市宝安区创业二路7号创业大厦5层510

TEL:0755-27817100        FAX: 0755-27817110

http://www.rfid17.com        jinqing31@163.com

低频测试电缆组件（DC—6GHz）

特性优势

- 低损耗、低驻波比

- 屏蔽性较高

- 半柔性

- 使用寿命长

- 重量轻

- 工作温度范围-55℃／+200℃

适用范围

- L波段军用及商用领域的设备内连接

- 工业控制领域

- 移动通信基站内模块设备的连接

- 微波信号源、微波矢量网络分析仪及频谱分析仪

- 微波系统设备连接

典型组件

产品型号：YD21606

◎ 组件长度：800mm

◎ 连 接 器：SMAm／SMAm

◎ 频率范围：DC－6GHz

◎ DC－3GHz： VSWR：≤1.15   IL：≤1.20dB

◎ 3－6GHz：  VSWR：≤1.25   IL：≤1.50dB

# Low frequency cable assemblies（DC—6GHz）

- Special Advantage

- Low loss, low VSWR

- High-performance shielding

- Semi-flexibility

- Long using life

- Low weight

- Operation temperature -55℃～+200℃

- Range Of Application

- Internal connection of L-band military and commercial equipment

- Industrial control area

- Module connection inside mobile communication base station

- Microwave signal source,microwave vector network analyzer and spectrum analyzer

- Microwave system equipment connection

# Typical assemblies

# Product Type：YD21606

◎ Assembly length： 800mm

◎ Connector：       SMAm／SMAm

◎ Range of frequency：DC－6GHz

◎ DC－3GHz： VSWR：≤1.15   IL：≤1.20dB

◎ 3－6GHz：  VSWR：≤1.25   IL：≤1.50dB

# N型测试电缆组件（DC—18GHz）

特性优势

- 低损耗、低驻波比

- 稳定的幅度和相位指标

- 屏蔽性较高

- 柔软性好，易于弯曲

- 使用寿命长

- 工作温度范围-55℃／+200℃

适用范围

- 高端通信系统

- 微波矢量网络分析仪

- 便携式驻波测试仪

- 频谱分析仪

- 微波信号源

- 雷达系统

- 航空航天子系统

- 卫星通信

- 军事高可靠性系统

典型组件

产品型号：YD21618

◎ 组件长度：800mm

◎ 连 接 器：Nm／Nm

◎ 频率范围：DC－18GHz

◎ DC－6GHz：VSWR：≤1.25   IL：≤0.80dB

◎ 6－18GHz：VSWR：≤ 1.35  IL：≤1.50dB

# Model N cable assembly（DC—18GHz）

# Special Advantage

- Low loss, low VSWR

- Stable amplitude and phase

- High-performance shielding

- Perfect flexure and easy to bend

- Long using life

- Operation temperature -55℃～+200℃

# Range Of Application

- High-end communication system

- Microwave vector network analyzer

- Portable standing-wave tester

- spectrum analyzer

- Microwave signal source

- Radar system

- Aviation and aerospace subsystem

- Satellite communication

- High reliability military system

# Typical assemblies

# Product Type：YD21618

◎ Assembly length： 800mm

◎ Connector：        Nm／Nm

◎ Range of frequency：DC－18GHz

◎ DC－6GHz：VSWR： ≤1.25   IL：≤0.80dB

◎ 6－18GHz：VSWR： ≤1.35   IL：≤1.50dB

3.5mm／SMA测试电缆组件（DC—26.5GHz）

特性优势

- 低损耗、低驻波比

- 屏蔽性较高

- 柔软性好，易于弯曲

- 使用寿命长

- 重量轻

- 工作温度范围-55℃／+165℃

适用范围

- 高端通信系统

- 微波矢量网络分析仪

- 便携式驻波测试仪

- 频谱分析仪

- 微波信号源

- 雷达系统

- 航空航天子系统

- 卫星通信

- 军事高可靠性系统

典型组件

产品型号：YD23265

◎ 组件长度：800mm

◎ 连 接 器：SMAm ／SMAm

◎ 频率范围：DC－27GHz

◎ DC－6GHz：   VSWR：≤1.10  IL：≤0.65dB

◎ 6－12GHz：   VSWR：≤1.15  IL：≤1.45dB

◎ 12－18GHz：  VSWR：≤1.25  IL：≤1.55dB

◎ 18－26.5GHz：VSWR：≤1.30  IL：≤2.15dB

3.5mm／SMA Cable Assemblies （DC—26.5GHz）

# Special Advantage

- Low loss, low VSWR

- High-performance shielding

- Perfect flexure and easy to bend

- Long using life

- Low weight

- Operation temperature -55℃～+165℃

# Range Of Application

- High-end communication system

- Microwave vector network analyzer

- Portable standing-wave tester

- spectrum analyzer

- Microwave signal source

- Radar system

- Aviation and aerospace subsystem

- Satellite communication

- High reliability military system

# Typical assemblies

# Product Type：YD23265

◎ Assembly length：  800mm

◎ Connector：       SMAm ／SMAm

◎ Range of frequency：DC－27GHz

◎ DC－6GHz：  VSWR：≤1.10   IL：≤0.65dB

◎ 6－12GHz：  VSWR：≤1.20   IL：≤1.45dB

◎ 12－18GHz： VSWR：≤1.25   IL：≤1.55dB

◎ 18－27GHz： VSWR：≤1.35   IL：≤2.15dB

2.4mm／2.92mm测试电缆组件（DC—40GHz）

特性优势

- 低损耗、低驻波比

- 屏蔽性较高

- 柔软性好，易于弯曲

- 使用寿命长

- 重量轻

- 使用频率高

- 耐环境型好

- 工作温度范围-55℃／+200℃

适用范围

- 高端通信系统

- 微波矢量网络分析仪

- 频谱分析仪

- 微波信号源

- 雷达系统

- 航空航天子系统

- 军事高可靠性系统

- 卫星通信

- 电子对抗

典型组件

产品型号：YD22440

◎ 组件长度：800mm

◎ 连 接 器：2.4mm M／2.4mm M

◎ 频率范围：DC－40GHz

◎ DC－6GHz：   VSWR：≤1.15   IL：≤0.60dB

◎ 6－12GHz：   VSWR：≤1.16   IL：≤1.30dB

◎ 12－18GHz：  VSWR：≤1.18   IL：≤2.00dB

◎ 18－26.5GHz：VSWR：≤1.20   IL：≤2.15dB

◎ 26.5－40GHz：VSWR：≤1.30   IL：≤3.00dB

2.4mm／2.92mm Cable Assemblies（DC—40GHz）

# Special Advantage

- Low loss, low VSWR

- High-performance shielding

- Perfect flexure and easy to bend

- Long using life

- Low weight

- High using frequency

- High environment adaptability

- Operation temperature -55℃～+200℃

# Range Of Application

- High-end communication system

- Microwave vector network analyzer

- spectrum analyzer

- Microwave signal source

- Radar system

- Aviation and aerospace subsystem

- High reliability military system

- Satellite communication

- Electronic counter measures

# Typical assemblies

# Product Type：YD22440

◎ Assembly length：  800mm

◎ Connector：       2.4mm M／2.4mm M

◎ Range of frequency：DC－40GHz

◎ DC－6GHz：    VSWR：≤1.15    IL：≤0.60dB

◎ 6－12GHz：    VSWR：≤1.16    IL：≤1.30dB

◎ 12－18GHz：   VSWR：≤1.18    IL：≤2.00dB

◎ 18－26.5GHz： VSWR：≤1.20    IL：≤2.15dB

◎ 26.5－40GHz： VSWR：≤1.30    IL：≤3.00dB

半刚电缆组件（DC—26.5/50GHz）

特性优势

- 低损耗、低驻波比

- 屏蔽性高

- 可靠性高

- 使用寿命长

- 重量轻

- 使用频率高

- 耐环境型好

适用范围

- 高端通信系统

- 微波仪器内部模块连接

- 移动通信基站

- 导航

- 军用雷达

- 武器系统

- 医疗设备

- 卫星通信

- 电子对抗

- 飞船

- 天线

典型组件

产品型号：YD23265S

◎ 组件长度：500mm

◎ 连 接 器：SMAm／SMAm

◎ 频率范围：DC－26.5GHz

◎ DC－6GHz：   VSWR：≤1.08  IL：≤0.50dB

◎ 6－18GHz：   VSWR：≤1.15  IL：≤1.05dB

◎ 18－26.5GHz：VSWR：≤1.25  IL：≤1.45dB

产品型号：YD22440S

◎ 组件长度：500mm

◎ 连 接 器：2.4mm M／2.4mm M

◎ 频率范围：DC－50GHz

◎ DC－6GHz：   VSWR：≤1.10    IL：≤0.50dB

◎ 6－18GHz：   VSWR：≤1.15    IL：≤1.60dB

◎ 18－26.5GHz：VSWR：≤1.20    IL：≤2.00dB

◎ 26.5－50GHz：VSWR：≤1.40    IL：≤3.00dB

# Semi-Rigid Cable Assemblies（DC—26.5/50GHz）

# Special Advantage

- Low loss, low VSWR

- High-performance shielding

- High reliability

- Long using life

- Low weight

- High using frequency

- High environment adaptability

# Range Of Application

- High-end communication system

- Module connection inside microwave equipment

- Mobile communication base station

- Navigation

- Military radar

- Weapon system

- Medical equipment

- Satellite communication

- Electronic counter measures

- Spaceship

- Antenna

# Typical assemblies

# Product Type：YD23265S

◎ Assembly length：  500mm

◎ Connector：       SMAm／SMAm

◎ Range of frequency：DC－26.5GHz

◎ DC－6GHz：    VSWR：≤1.08   IL：≤0.50dB

◎ 6－18GHz：    VSWR：≤1.15   IL：≤1.05dB

◎ 18－26.5GHz： VSWR：≤1.25   IL：≤1.45dB

# Product Type：YD22440S

◎ Assembly length：  500mm

◎ Connector：       2.4mm M／2.4mm M

◎ Range of frequency：DC－50GHz

◎ DC－6GHz：    VSWR：≤1.10     IL：≤0.50dB

◎ 6－18GHz：    VSWR：≤1.15     IL：≤1.60dB

◎ 18－26.5GHz： VSWR：≤1.20     IL：≤2.00dB

◎ 26.5－50GHz： VSWR：≤1.40     IL：≤3.00dB

电缆组件使用注意事项

电缆组件是一种系统连接测试耗材，不正确的操作，频繁的使用会缩短电缆的使用寿命。正常情况下，连接器的插拔次数约为500~1000次，电缆的弯曲次数大于5000次

使用注意事项
　　●　电缆在使用前应检查所用的电缆连接器与设备端接口是否匹配。

●　使用电缆时，必须使用力矩扳手旋紧，同时不能超过连接器规定的最大力矩。正确的连接器连接方法是：将同类型连接器的阴头和阳头对准后，一只手握住阴头，另一只手旋转阳头的锁紧螺母，同时保证内外导体不相对转动，严禁旋转阴头连接。
　　●　使用电缆时应尽量减少弯曲次数，否则会缩短电缆的使用寿命。由于使用环境较为复杂，需要弯曲时，弯曲半径不能小于电缆本身的最小弯曲半径。

●　使用电缆时，应保证不受任何冲击和挤压，任何的冲击、挤压都可能会破坏电缆的电气性能，严禁私自加装电缆保护套，以免破坏电缆的机械结构，缩短其使用寿命。

存放环境要求：

产品应存放于温度为-10(C～40(C，相对湿度≤75(，防灰尘、无腐蚀性的环境内。