WIRELESS  DYNAMOMETER

USER   MANUAL

Model: AXL-W3

Shanghai ang Xuan Instrument Co.,LTD    COPYRIGHT

USER MANUAL                                                             ERT07.023 SSE

TABLE OF CONTENTS

SAFE OPERATION GUIDE…………………………………………......…...……….…..…2

CHAPTER 1	FEATURES AND SPECIFICATION.................................................... 3

1. Features..............................................................................................................3

2. Main technical data................................................................................................3

3. Specification.................................................................................. ............................4

4. Appearance illustration............................................................................................4

5. Power supply..................................................................... ...............................5

CHAPTER 2	DISPLAY AND KEYS.......................................................................... 5

1. LCD display..........................................................................................................5

2. Keys......................................................................................................................6

CHAPTER 3	WIRELESS INDICATOR OPERATION GUIDE................................... .6

CHAPTER 4	DYMOMETER FUNCTION GUIDE...................................... ...............7

1. On/off............................................................................................................. …...... ..7

2. Zero...................................................................................................................8

3. Tare....................................................................................................................8

4. Peak Hold..........................................................................................................8

5. Accumulation.....................................................................................................9

6. Accumulation Search...........................................................................................9

7. Accumulation Clear..................................................................................................9

8. Battery Voltage ……...........................................................................................9

9. Unit ………............................................................................................................9

10. Return................ ..............................................................................................10

11. Set point..........................................................................................................10

.

CHAPTER 5 PARAMETER SETTING & CALIBRATION...........................................11

1. Key function........................................................................................................11

2. Parameter setting................................................................................................11

3. Calibration..........................................................................................................13

CHAPTER 6 SIGNAL ILLUSTRATION.........................................................................14

CHAPTER 7 TROUBLESHOOTING GUIDE................................................................15

CHAPTER 8 RS232 PROTOCOL.................................................................................16

USER MANUAL                           1                                 ERT07.023 SSE

SAFE OPERATION GUIDE：

1.Do not make lifts beyond rated load capacity of the dynamometer, shackle.

2.Do not perform overhead weighing. Stay clear when Dynamometer is in operation.

3. Do not perform weighing under strong wind condition which may cause incorrect reading.

4. Do not perform weighing under environment of temperature rapid changes in  which may cause incorrect reading.

5. Do not attempt to open this Dynamometer, no user serviceable parts inside.

6. Do not remove wire rope stopper from hook. For safety reasons, always apply it.

7. Remove all loads from shackle or hook when not in used.

8. Before weighing, check and make sure that all hanging /load- receiving elements / devices are in good condition.

9. Check hook, shackle, safety pins, and latches periodically. Contact your dealer for parts replacement in case defect, deform or wearing is found.

10. Always lift loads vertically.

USER MANUAL                           2                                ERT07.023 SSE

CHAPTER 1   FEATURES  AND  SPECIFICATIONS

Introduction:

AXL-W3 wireless Dynamometer is an extremely well-built instrument for industry use ,as a standard wireless tool offer universal applications, Whether used as conventional crane weigher or to measure force, AXL-W3 wireless Dynamometer is microprocessor controlled for precision accuracy, parameter setting and calibration is easy to operate through wireless indicator.

1. Features

● Rugged construction, Aluminum and alloy steel capacities are powder coated.

● Accuracy: 0.05% for 1-50t, 0.1% for above 50t capacity.

● Dual direction wireless communication

● All functions and units are clearly display on the LCD (with backlighting)

● Digits are 1 inch high for easy distant viewing.

● Two user programmable Set-Point can be used for safety and warning

applications or for limit weighing.

● The dynamometer is powered by 3 standard “LR6(AA)”size alkaline batteries.

● All commonly used internationally recognized units are available:

kilograms (kg), short Tons(t), pounds(lb), Newton and kilo-newton(kN).

● Operation through wireless handheld indicator, easier to calibrate

(with password)

● 4 local mechanical keys: ”ON/OFF”,”ZERO”,”PEAK” and ”Unit Change”.

● Low battery warning.

● RF wireless handheld indicator is powered by 4 standard “LR6(AA)”size

alkaline batteries.

2. Main technical data

| Display | 25mm (1’’) 5digits LCD with backlight |
| --- | --- |
| Power on zero range | 20% F.S. |
| Manual Zero Range | 4% F.S. |
| Tare Range | 100% F.S. |
| Stable Time | ≤5 seconds |
| Overload Indication | 100% F.S. + 9e |
| Max. Safety Load | 125% F.S. |
| Ultimate Load | 400% F.S. |
| Dynamometer battery | “LR6(AA)”size alkaline batteries. 1.5Vx3 |
| Indicator battery | “LR6(AA)”size alkaline batteries. 1.5Vx4 |
| Operating Temp. | - 10℃ ~ + 40℃ |
| Operating Humidity | ≤85% RH under 20℃ |
| Wireless Distance | Min. 80m(default) , 200m(optional) |
| Wireless Frequency | 2.4GHz(default),433MHz,860MHz(optional) |

USER MANUAL                             3                                ERT07.023 SSE

3. Specification

| Model | Capacity(kg) | Min.Weigh(kg) | Division(kg) | Total counts (n) |
| --- | --- | --- | --- | --- |
| AXL-W3-01 | 1000 | 10 | 0.5 | 2000 |
| AXL-W3-02 | 2000 | 20 | 1 | 2000 |
| AXL-W3-03 | 3000 | 20 | 1 | 3000 |
| AXL-W3-05 | 5000 | 40 | 2 | 2500 |
| AXL-W3-10 | 10000 | 100 | 5 | 2000 |
| AXL-W3-20 | 20000 | 200 | 10 | 2000 |
| AXL-W3-30 | 30000 | 200 | 10 | 3000 |
| AXL-W3-50 | 50000 | 400 | 20 | 2500 |
| AXL-W3-100 | 100000 | 1000 | 50 | 2000 |
| AXL-W3-200 | 200000 | 2000 | 100 | 2000 |

4. Appearance illustration

Cap: 1-5t                              Cap: 10-200t

DIMENSIONS(Dimensions shown are nominal and subject to tolerances)

| MODEL | CAP | A(mm) | B(mm) | C(mm) | D(mm) | φ(mm) | H(mm) | Material |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| AXL-W3-1 | 1t | 245 | 112 | 37 | 190 | 43 | 335 | Aluminum |
| AXL-W3-2 | 2t | 260 | 123 | 37 | 195 | 51 | 365 | Aluminum |
| AXL-W3-3 | 3t | 260 | 123 | 37 | 195 | 51 | 365 | Aluminum |
| AXL-W3-5 | 5t | 285 | 123 | 57 | 210 | 58 | 405 | Aluminum |
| AXL-W3-10 | 10t | 320 | 120 | 57 | 230 | 92 | 535 | Alloy Steel |
| AXL-W3-20 | 20t | 375 | 128 | 74 | 260 | 127 | 660 | Alloy Steel |
| AXL-W3-30 | 30 | 420 | 138 | 82 | 280 | 146 | 740 | Alloy Steel |
| AXL-W3-50 | 50t | 465 | 150 | 104 | 305 | 184 | 930 | Alloy Steel |
| AXL-W3-100 | 100t | 570 | 190 | 132 | 366 | 229 | 1230 | Alloy Steel |
| AXL-W3-200 | 200t | 720 | 265 | 183 | 440 | 280 | 1362 | Alloy Steel |

USER MANUAL                               4                                ERT07.023 SSE

WEIGHTS

| Model | AXL-W3-1 | AXL-W3-2 | AXL-W3-3 | AXL-W3-5 | AXL-W3-10 |
| --- | --- | --- | --- | --- | --- |
| Unit Weight(kg) | 1.6 | 2.1 | 2.1 | 2.7 | 10.4 |
| Weight with shackles(kg) | 3.1 | 4.6 | 4.6 | 6.3 | 24.8 |
| Model | AXL-W3-20 | AXL-W3-30 | AXL-W3-50 | AXL-W3-100 | AXL-W3-200 |
| Unit Weight(kg) | 17.8 | 25 | 39 | 81 | 210 |
| Weight with shackles(kg) | 48.6 | 73 | 128 | 321 | 776 |

5. Power supply

Dynamometer battery: “LR6(AA)”size alkaline batteries. 1.5VX3

Indicator battery: “LR6(AA)”size alkaline batteries. 1.5VX4

Current: the dynamometer average current is about DC 35mA, 3pcs new batteries can be used for about 40hours under continous working.

Wireless indicator average current is about DC 28mA, 4pcs new batteries can be used for about 80hours under continous working.

Low battery warning: When the digits flashes, it means the battery needs to be replaced. The Dynamometer or wireless indicator will power off automatically after one hour without operation.

CHAPTER 2   DISPLAY AND KEYS

1. LCD DISPLAY

a.  25mm (1’’) 5digits LCD with all functions and units.

b.  :  Wireless signal, it Appear means signal stable, it disappear while signal miss.

it flash means signal weak.

c.   :  Battery Voltage, : Full, : Low, : Empty

d.   PEAK：Current value is Peak Hold value(maximum value).

e.   MEM：Appear one time when Parameter or calibration value storage. long time

appearance means current value is Accumulation data.

f.   STB:  Stable Status.

g.   kN:  “kilonewton”, N：“Newton”. Tare status “N” will flash.

h.   t ：“ton”

i.   lb ：“pound”

j.   kg ：“kilogram ”

USER MANUAL                             5                               ERT07.023 SSE

2. Keys

a. ON/OFF key

1．Press “ON/OFF” Key 1 Second, the Dynamometer turn on.

2．In ON status，Press “ON/OFF” Key 1 Second，the Dynamometer turn off.

b. ZERO key

When Dynamometer switch on with no load,  but there are small digits on the screen, press this key to obtain the zero reading.

c. UNIT key

Press UNIT  key,  the unit on LCD will display circlely as follows: “kg”→ “lb” →“N” → “kN”→ “t”→ “kg”  .

d. PEAK key

When load is changing, press this key will catch and display the maximum reading of the load.

Press this key again, reading will return to normal.

CHAPTER 3  WIRELESS INDICATOR OPERATION GUIDE

a. 【ON/OFF】

1．Press “ON/OFF” Key 1 Second, the indicator turn on.

2．In ON status，Press “ON/OFF” Key 1 Second，the indicator turn off.

b. 【ZERO】

1. In testing status ,there are small digits on screen, press this key to obtain the zero reading.

2.In Parameter Setting status，it used as scrolling up digit.

c. 【TARE】

1. When there is tare weight such as container, after the reading stable, press this key,  it will display “0”, and “N” indicator Flash.

2. Put the goods into container, the dynamometer will display goods net weight.

3. If move goods and container, the dynamometer will display minus value of tare weight.

4. In Parameter Setting status, it used as digits movement.

USER MANUAL                             6                               ERT07.023 SSE

d. 【MODE】

Used as function shift, or be combined with other keys.

◆ Press【MODE】key once, it display “OFF”, press【ENTER】Key , it will wireless turn off dynamometer, and indicator display “noSIG”, means no singal.

◆ Press【MODE】key twice, it display “SETUP”, Press 【ENTER】Key access Parameter Setting status. After setting finish, press 【MODE】key  to confirm setting and back to test mode.

◆ Press【MODE】key 3  times, it  display “dC”, Press【ENTER】Key  to read current  battery voltage, press【MODE】key again back to test mode.

◆ Press 【MODE】key 4 times, it display “Unit”, Press 【ENTER】Key access unit selection. Press【ZERO】key to select unit, press【MODE】key again back to test mode.

◆ Press【MODE】key 5 times, it display “ACCU”, Press 【ENTER】Key access Accumulation status, press【MODE】key again back to test mode.

◆ Press【MODE】 key 6 times, it display “SACCU”, Press【ENTER】 Key

access Accumulation Search status, press【MODE】key again back to test mode.

◆ Press【MODE】 key 7 times, display “CLEAr”, Press【ENTER】 Key access Accumulation clear status, display “CLr  1”, Press【TARE】Key, display“noCLr”. press【MODE】key again back to test mode.

◆ Press【MODE】 key 8 times, display “CLIbr”, Press【ENTER】Key enter into calibration program, after calibration finish, press【MENU】key back to test MENU. Detail see Pg.13

◆ Press【MODE】 key 9 times, it display “ESC”, Press 【ENTER】Key and It will back to test mode.

e. 【ENTER】

Used as function selection, normally combined with 【MODE】Key

f. 【PEAK】

When load is changing, press this key will catch and display the maximum reading of the load.

Press this key again, reading will return to normal.

CHAPTER 4  DYNAMOMETER FUNCTION GUIDE

Note：(  ) means the  key on the dynamometer

【 】means the key on the indicator

〖 〗means the display content

1. ON/OFF

◆TURN ON dynamometer

| OPERATION | DISPLAY | ILLUSTRATION |
| --- | --- | --- |
| (ON/OFF) | 〖88888〗 | Display twice, self test |
|  | 〖 Ert 〗 | Display twice， abbreviation of |
|  | 〖u=3.72〗 | Display current software version |
|  | 〖CH=E3〗 | Display current wireless channel E3 |
|  | 〖 5000〗 | Display capacity, e.g. 5t |
|  | 〖U=3.98〗 | Display current battery voltage is 3.98 |
|  | 〖–––––〗 | Waiting stable |
|  | 〖 0〗 | Display curent load, generally is 0 |

USER MANUAL                                7                               ERT07.023 SSE

◆TURN ON indicator

| OPERATION | DISPLAY | ILLUSTRATION |
| --- | --- | --- |
| 【ON/OFF】 | 〖88888〗 | Display twice, self test |
|  | 〖 Ert 〗 | Display twice， abbreviation of |
|  | 〖u 1.2〗 | Display current software version |
|  | 〖CH=E3〗 | Display current wireless channel E3 |
|  | 〖U=3.98〗 | Display current battery voltage is 3.98 |
|  | 〖–––––〗 | Waiting stable |
|  | 〖 0〗or〖noSIG〗 | If display 0, means the indicator can communicate with the dynamometer, if display noSIG, means no signal from dynamometer |

◆TURN OFF dynamometer

| 1 | Manual Power OFF | Press (ON/OFF) Key 1 Second |
| --- | --- | --- |
| 2 | RemotePower OFF | Press【MODE】Key to select “OFF”, press【ENTER】Key |
| 3 | Auto Power OFF | Choose turn off method in parameter setting, the dynamometer will display〖 -〗after no operation at 15minutes to save power, and it will turn off automatically after 60minutes. |

◆TURN OFF indicator

| 1 | Manual Power OFF | Press 【ON/OFF】 Key 1 Second |
| --- | --- | --- |
| 2 | Auto Power OFF | The indicator will turn off automatically after 3 minutes if no operation |

2. ZERO

|  | OPERATION | DISPLAY | When Dynamometer turn on, generally it displays〖 0〗,if display small digits when no load, press this key. |
| --- | --- | --- | --- |
| 1 | Press（ZERO） | 〖 0〗 |  |
| 2 | Press【ZERO】 |  |  |

3. TARE

|  | OPERATION | DISPLAY | After turn on, hanging tare weight such as sling, cable at first, press this key, “TARE” light on, then the scale will display net weight of the goods. |
| --- | --- | --- | --- |
|  | Press【TARE】 | 〖 0〗 |  |

4.PEAK HOLD

| OPERATION | ILLUSTRATION |
| --- | --- |
| Press (PEAK) | Catch and display Maximum value of changing load |
| Press (PEAK) | reading return to normal |

USER MANUAL                                8                               ERT07.023 SSE

5.ACCUMULATION

| OPERATION | DISPLAY | ILLUSTRATION |
| --- | --- | --- |
| Press 【MODE】 key 5 times | 〖 ACCU〗 |  |
| Press【ENTER】 | 〖No***〗 | Current accumulation time |
|  | 〖H****〗 | Front four digits of total value |
|  | 〖L****〗 | Rear four digits of total value |

After display above contents twice, the dynamometer will return automatically.

6.ACCUMULATION SEARCH

| OPERATION | DISPLAY | ILLUSTRATION |
| --- | --- | --- |
| Press 【MODE】 key 6 times | 〖SACCU〗 |  |
| Press 【ENTER】 | 〖No***〗 | Current accumulation time |
|  | 〖*****〗 | Current weight reading |
|  | 〖H****〗 | Front four digits of total value |
|  | 〖L****〗 | Rear four digits of total value |
| Press 【MODE】key again |  | Return |

Press【TARE】and【ZERO】can check different times weight and accumulation.

7. ACCUMULATION CLEAR

| OPERATION | DISPLAY | ILLUSTRATION |
| --- | --- | --- |
| Press【MODE】key 7 times | 〖CLEAr〗 |  |
| Press 【ENTER】 | 〖CLr 1〗 | Ask if you want to clear or not |
|  | 〖noCLr〗 | Press【MODE】key Cancel clear |
|  | 〖88888〗 | Press【ENTER】key Confirm clear |

8. BATTERY VOLTAGE

| OPERATION | DISPLAY | ILLUSTRATION |
| --- | --- | --- |
| Press 【 MODE 】 key 3 times, Display “dC”, press 【ENTER】 key. | 〖U *.**〗 | Display current battery voltage |
| Press 【MODE】 key again |  | Return |

Note：Battery voltage normally between 〖U 3.50〗to 〖U 4.70〗, if below 〖U 3.10〗,

the display will flash, Battery should be replaced.

9. UNIT

|  | OPERATION | DISPLAY | ILLUSTRATION |
| --- | --- | --- | --- |
| 1 | Press【MODE】key 4 times | 〖UnIt 〗 |  |
|  | press 【 ENTER 】 key | 〖Un=0〗 | Un=0, the unit is kg, press【 ZERO】to select unit from 0-4, 1 means lb,2 means N, 3 means KN, 4means ton. |
|  | Press 【MODE】 key | 〖 0〗 | Confirm unit chosen and return |
| 2 | Press (UNIT) | 〖Un =0〗 | The dynamometer will display kg, lb, N, kN, ton circlely |

USER MANUAL                                9                                ERT07.023 SSE

10. RETURN

| OPERATION | DISPLAY | ILLUSTRATION |
| --- | --- | --- |
| Press【MODE】key 9 times | 〖 ESC〗 |  |
| press 【 ENTER 】 key | 〖 0〗 | Return to normal testing status |

11. SET POINT

There are two user programmable Set-Point can be used for safety and warning applications

or for limit weighing.

_          1 LO   SP1  1 HI        2 LO  SP2  2 HI

| OPERATION | DISPLAY | ILLUSTRATION |
| --- | --- | --- |
| Press【MODE】key twice | 〖SETUP〗 | Confirm, enter into parameter setting program |
| Press 【ENTER】 | 〖SP1 〗 | Set point 1 |
| Press【ENTER】to confirm | 〖1 OFF〗 | New dynamometer, it display 1 OFF, if parameter set, it display set value. |
| Press【ZERO】 to choose | 〖1 HI〗or 〖1 LO〗 | There are 3 choice,1 OFF means you don’t set point, 1 HI means the indicator will alarm when load exceed the value you set, 1 LO means the indicator will alarm when load smaller than the value |
| Press【ENTER】to confirm | 〖02000〗 | New dynamometer it display 02000, if parameter set, the screen display set value. |
| Press【 ZERO 】and【TARE】to change value | 〖01000〗 | Set “1 HI” or “1 LO” Value. e.g. 1000kg |
| Press【ENTER】to confirm | 〖 SP2〗 | Set point 2 |
| Press【ENTER】to confirm | 〖2 OFF〗 | New dynamometer, it display 2 OFF, if parameter set, it display set value. |
| Press【ZERO】to choose | 〖2 HI〗or 〖2 LO〗 | There are 3 choice,2 OFF means you don’t set point, 2 HI means the indicator will alarm when load exceed the value you set, 2 LO means the indicator will alarm when load smaller than the value |
| Press【ENTER】to confirm | 〖01200〗 | New dynamometer it display 01200, if parameter set, the screen display set value. |
| Press【 ZERO 】and【TARE】to change value | 〖03000〗 | Set “2 LO” or “2 HI” Value. e.g.3000kg |

If you needn’t to set point, you only need to press 【ENTER】until it display next function

〖g=  〗

USER MANUAL                               10                               ERT07.023 SSE

CHAPTER 5   PARAMETER SETTING & CALIBRATION

parameter setting and calibration will be operated through wireless indicator

1.Key function

| KEY | FUNCTION |
| --- | --- |
| 【TARE】 | Move digit |
| 【ZERO】 | Set value up |
| 【MODE】 | Storage and exit |
| 【ENTER】 | Confirm |

2. Parameter setting

| OPERATION | DISPLAY | ILLUSTRATION |
| --- | --- | --- |
| Press【MODE】key twice | 〖SETUP〗 | Confirm, enter into parameter setting program |
| Press【ENTER】 | 〖FS=06〗 | New dynamometer, it display FS=06 ，if dynamometer calibrated, it will display capacity. |
| Press【ZERO】to choose | 〖FS=05〗 | Choose capacity, the screen display02/03/05/06/10/ 15/20/30/50/60/75/80 circularly，take cap:5000kg/2kg as example, choose FS=05, See following list about FS, Id, Pt chosen. |
| Press【ENTER】 to confirm | 〖Id=02〗 | New dynamometer , the screen display Id=02, if dynamometer calibrated, it will display calibrated division. |
| Press【ZERO】 to choose | 〖Id=02〗 | Choose division, it display 01/02/05/10/20circularly. 5000kg dynamometer division is 2kg, so choose Id=02 |
| Press【ENTER】 | 〖Pt=0〗 | New dynamometer, it display Pt=0, if dynamometer calibrated, it will display calibrated decimal position |
| Press【ZERO】 to choose | 〖Pt=0〗 | Choose decimal position, the screen display 0/1/2/3 circularly, 0=xxxxx, 1=xxxx.x, 2=xxx.xx, 3=xx.xxx，Cap.5000kg ,we choose Pt=0 |
| Press【ENTER】 to confirm | 〖Ab=24〗 | Display zero range , A: zero range by hand; B: zero range automatically, 0~5 total 6 options: 0=0%F. S; 1=2%F.S; 2=4%F.S; 3=10%F.S; 4=20%F.S; 5=50%F.S, Generally Don’t change this parameter. |
| Press【ENTER】 to confirm | 〖Cd=11〗 | New dynamometer, the screen display Cd=11,if Dynamometer calibrated, it display calibrated value. |

USER MANUAL                               11                               ERT07.023 SSE

| Press【ZERO】 to choose | 〖Cd=12〗 | C: zero-tracking range, 0~5 total 6 options; 0=0d; 1=0.5d; 2=1d; 3=1.5d; 4=2d; 5=2.5d d: display speed，0~2 total 3 options; 0=slow; 1=average; 2=fast; before calibration, set Cd=00 to achieve high accuracy, after calibration, set Cd=11 again, generally choose Cd==12 when ex-stock.. |
| --- | --- | --- |
| Press【ENTER】 to confirm | 〖LL=2〗 | New dynamometer, it display LL=2, if dynamometer calibrated，it display calibrated value. |
| Press【ZERO】 to choose | 〖LL=1〗 | LL：filter parameter，0~5 total 6 options， from smallest to biggest ， before calibration, set LL=0, after calibration, set LL=1 , generally choose LL=1 when ex-stock.. |
| Press【ENTER】 to confirm | 〖Un=0〗 | New dynamometer, it display Un=0, if dyna-link calibrated，the screen display calibrated unit. |
| Press【ZERO】 to choose | 〖Un=0〗 | Choose unit，Un=0：kg, Un=1: lb, Un=2: N,Un=3: KN, Un=4: ton, Generally, choose Un=0 when ex-stock. |
| Press【ENTER】 to confirm | 〖OFF 1〗 | New dynamometer, it display OFF 1,if dynamometer calibrated，it display calibrated value. |
| Press【ZERO】 to choose | 〖OFF 2〗 | Choose turn off method, 0~2 total 3 options; 0: turn off by hand; 1: if no operation, the screen display ----- after 15minutes to save power; 2: if no operation, the screen display ----- after 15minutes, and turn off automatically after 60minutes. Generally, choose OFF=2 when ex-stock. |
| Press【ENTER】 | 〖SP1 〗 | Set point 1 |
| Press【ENTER】to confirm | 〖1 OFF〗 | New dynamometer, it display 1 OFF, if parameter set, it display set value. |
| Press【ZERO】 to choose | 〖1 HI〗or 〖1 LO〗 | There are 3 choice,1 OFF means you don’t set point, 1 HI means the indicator will alarm when load exceed the value you set, 1 LO means the indicator will alarm when load smaller than the value |
| Press【ENTER】to confirm | 〖02000〗 | New dynamometer it display 02000, if parameter set, the screen display set value. |
| Press【 ZERO 】and【TARE】to change value | 〖01000〗 | Set “1 HI” or “1 LO” Value. e.g. 1000kg |
| Press【ENTER】 | 〖 SP2〗 | Set point 2 |
| Press【ENTER】to confirm | 〖2 OFF〗 | New dynamometer, it display 2 OFF, if parameter set, it display set value. |
| Press【ZERO】to choose | 〖2 HI〗 or 〖2 LO〗 | There are 3 choice,2 OFF means you don’t set point, 2 HI means the indicator will alarm when load exceed the value you set, 2 LO means the indicator will alarm when load smaller than the value |

USER MANUAL                               12                               ERT07.023 SSE

| Press【ENTER】to confirm | 〖01200〗 | New dynamometer it display 01200, if parameter set, the screen display set value. |
| --- | --- | --- |
| Press【 ZERO 】and【TARE】 | 〖03000〗 | Set “2 LO” or “2 HI” Value. e.g.3000kg,input 3000 |
| Press【ENTER】 | 〖g= 〗 | acceleration of gravity |
| Pres【 ENTER】Press【 ZERO 】and【TARE】to change value | 〖9.7930〗 | New dynamometer , it display 9.7930, if dynamometer calibrated, it display calibrated value. user can change it according to local area g value, the value range is 9.783-9.832, |
| Press【MODE】key | 〖 End 〗 〖 0〗 | Confirm above parameter setting，Exit parameter setting program. |

.       The capacity you choose relate to division, decimal position, below is detail list:

| CAPACITY/DIVISION | FS （CAP） | Id (DIVISION) | Pt（Decimal position） |
| --- | --- | --- | --- |
| 1000kg/0.5kg | 10 | 05 | 1 |
| 2000kg/1kg | 02 | 01 | 0 |
| 3000kg/1kg | 03 | 01 | 0 |
| 5000kg/2kg | 05 | 02 | 0 |
| 10000kg/5kg | 10 | 05 | 0 |
| 15000kg/5kg | 15 | 05 | 0 |
| 20000kg/10kg | 20 | 10 | 0 |
| 30000kg/10kg | 30 | 10 | 0 |
| 50000kg/20kg | 50 | 20 | 0 |

100t, 200t use specail software, no need to set FS,Id,Pt.

- Calibration

User must set all parameter before calibration

| OPERATION | DISPLAY | ILLUSTRATION |
| --- | --- | --- |
| Turn on dynamometer and indicator | 〖 0〗 | Take Cap:5000kg dynamometer as example , make sure it display〖 0〗before calibration, you can hang tare weight first, then turn on to get zero reading |
| Press【 MODE 】 key 8 times, | 〖CLIbr〗 | Access calibration Status |
| Press 【 ENTER 】key | 〖CAL 1〗 | Enter into one point calibration program |
| Press 【 ENTER 】key | 〖CALSP〗 | Zero point calibration |
| Press 【 ENTER 】key | 〖LoAd 〗 | Hanging standard weight, e.g. 3000kg Waiting until STB signal on screen |
| Press 【 ENTER 】key | 〖05000〗 | Display capacity you choose in parameter setting，and first digit flash，Do wait until “STB” signal display on screen. |
| Press【 ZERO 】and【TARE】key | 〖03000〗 | press 【 ZERO 】to change value, press【 TARE】 to move the digit |
| Press【 MODE 】 key | 〖-------〗 | Confirm and storage |

USER MANUAL                               13                               ERT07.023 SSE

|  | 〖 -oL- 〗 |  |
| --- | --- | --- |
|  | 〖End〗 | Calibration finish |
|  | 〖 3000〗 |  |

Attention: the standard load should be more than 20% capacity, it’s better to use full capacity standard load

CHAPTER 6	 DISPLAY	ILLUSTRATION

| DISPLAY | ILLUSTRATION | REMARK |
| --- | --- | --- |
| 〖noSIg〗 | Without wireless signal | Distance too far. |
| 〖SEtUP〗 | Enter into parameter setting |  |
| 〖UAdJ 〗 | Enter voltage calibration |  |
| 〖LoAd〗 | Calibration point |  |
| 〖¯ ¯ ¯ ¯ ¯ 〗 | Exceed high limit | Tare weight can’t exceed full capacity |
| 〖﹍﹍ 〗 | Exceed low limit | Tare weight can’t be negative |
| 〖-----〗 | Waiting stable |  |
| 〖Err10〗 | Weight less than Min. Capacity | Can’t accumulate the value |
| 〖Err11〗 | Accumumated times overflow | Can’t accumulate after 30times |
| 〖Err12〗 | Accumulated weight overflow | Can’t accumulate after 99999 |
| 〖Err13〗 | Error in repeat accumulation | Can’t accumulate one weight repeatedly |
| 〖no***〗 | Current accumulation times |  |
| 〖H****〗 | Front four digit of accumulated | Total weight=front four digit + rare four digit |
| 〖L****〗 | Rare four digit of accumulated | Total weight=front four digit + rare four digit |
| 〖 CLr 〗 | Ask if you really want to delete accumulated weight | In case error deletion |
| 〖noCLr〗 | Give up deletion |  |
| 〖88888〗 | Confirm deletion |  |
| 〖 ¯ ¯ ¯ 〗 | Input value is too large | When you input tare or weight value |
| 〖 ﹍ 〗 | Input value is too small | When you input tare or weight value |
| 〖noACC〗 | No any accumulated content | when you check accumulation |
| 〖-oL0- 〗 | Overload warning | Tare + Net weight exceed full capacity + 9e |
| 〖-oL1- 〗 | Overload warning | Tare + Net weight exceed full capacity 125% |
| 〖-Lb- 〗 | Low battery warning | Turn off automatically one minute later |
| 〖U*.**〗 | The voltage of current battery |  |
| 〖 End 〗 | End | when parameter setting or calibration ready |
| 〖 OFF 〗 | Turn off |  |
| 〖Unstb〗 | Input value before STB light on |  |

USER MANUAL                                14                               ERT07.023 SSE

CHAPTER 7  TROUBLESHOOTING GUIDE

| PROBLEM | POSSIBLE CAUSE | SOUTION |
| --- | --- | --- |
| No display | Defective battery | Replace |
|  | Defective button | Requires authorized service |
|  | Power button not properly pressed | Press ON/OFF key firmly in three seconds |
| Digits flash | Low battery | Replace battery |
| Display doesn’t respond to load changes | Faulty load cell or PCB | Requires authorized service |
|  | Out of calibration | Re- calibration |
| Display experiences excessive Zero drift between weighment | Dynamometer do not stabilize after turning on | After turning on, heating 3-5 minutes. |
| Displayed weight shows large error | Dynamometer not Zeroed before applying weight | Depress ZERO before applying weight |
|  | Requires recalibration | See calibration |
|  | Kg/lb wrong selection | See operation |
| Wireless distance shortened | Wireless indicator’s battery is low | Replace battery. |

USER MANUAL                               15                               ERT07.023 SSE

CHAPTER 8     RS232  PROTOCOL

Port :         COM1

Baud Rate:  4800

Data Bits :     8

Stop Bits :    1

Parity :       None

ASCII Code and Binary hybrid transmission

| = | FLAG (1Byte) | Unit | Sign and Decimal |
| --- | --- | --- | --- |
|  | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | (1Byte) | (1Byte) |
| preamble | S T ABL E | O V E R L O A D | T A R E | H O L D | P E A K | B E T T E R Y | SP A L A R M |  | 0x30：kg 0x31：Lb 0x32：N 0x33：kN 0x34：t | (+ and -) sign: High 4 bits Decimal: Low 4 bits |
| = | 0: no 1: Y E S | 0: no 1: Y E S | 0: no 1: Y E S | 0: no 1: Y E S | 0: no 1: Y E S | 0: L O W | 0: no 1: Y E S |  |  | 0:POSITIVE 1:NEGATIVE 0:No Decimal 1:1 Decimal 2:2 Decimal 3:3 Decimal |

| TTTTT | , | NNNNN/PPPPP |  |
| --- | --- | --- | --- |
| 5Byte | 1Byte | 5Byte |  |
| Tare value | Separate symble | Net value and Peak value |  |
| 0x30~0x39 Overload: 3SP+OL |  | 0x30~0x39 Overload: 3SP+OL |  |

Example:

67.8kg:  (F1 F2 F3 F4 F5 F6 F7 F8 )30 01 30 30 36 37 38，30 30 36 37 38

-68.1lb:  (F1 F2 F3 F4 F5 F6 F7 F8 )31 F1 30 30 36 37 38，30 30 36 37 38

6.78kg:  (F1 F2 F3 F4 F5 F6 F7 F8 )30 02 30 30 36 37 38，30 30 36 37 38

USER MANUAL                               16                               ERT07.023 SSE